## Slide 1: Camera Electrical and Network Info
Simulated Phonomicrosurgery Station

## Slide 2
Camera 1
Camera 2
POE Switch
PC
HW Trigger
Gigabit Ethernet
Digital
Low : 0 V
High: > 2.2 V (5-15 mA)
Camera Wiring
04/05/2011
Camera 1*
Camera 2*
POE Switch
PC
Signal Splitter
Ethernet
BNC
Signal Generator
BNC/DIN
*Cameras must be connected to powered ports on POE Switch
Signals
Physical Connections

## Slide 3
Splitter Box
MAX627CP+
1
2
3
4
8
5
6
7
Sig Gen
C1
2
5
C2
2
5
+5V
Low : 0 V
High: 3.3 V
Schematic
Basler acA640-100gc Pin Diagram
Splitter Box Diagram
+5V Power Source
Barrel Connector
To Camera Trigger Signals
BNC @ Splitter Box
Mini-DIN @ Camera
From Sig. Gen 3.3V Trigger Source
BNC @ Splitter Box
BNC @ Signal Generator

## Slide 4
Camera Network Configuration
04/23/2011
Network Adapter
Realtek PCIe GBE Family Controller (Motherboard).
IP Configuration : Fixed IP (TCP/IPv4)
IPv4 Address 172.16.0.1
IPv4 Subnet Mask 255.255.0.0
Right Camera
S/N: 21058262
MAC: 00:30:53:10:25:D6
IP Configuration: Fixed IP (TCP/IPv4)
Config Name RIGHT_CAM
IPv4 Address 172.16.0.3
IPv4 Subnet Mask 255.255.0.0
Left Camera
S/N: 21058246
MAC: 00:30:53:10:25:C6
IP Configuration: Fixed IP (TCP/IPv4)
Config Name LEFT_CAM
IPv4 Address 172.16.0.2
IPv4 Subnet Mask 255.255.0.0
Camera IP Configuration